## Slide 1: EECT/CE 6325 Final Project(4-bit calculation)
Xiongtao Zhang
yuyang hsieh

## Slide 2: Functionality
the output waveforms simulated by HSPICE meet all the expected value and all processing completed within one clock cycle

## Slide 3: LVS + DRC passed

## Slide 4: Design choices
The design contains 2 computation modules to perform addition, subtraction, multiplication, division; 1 MUX to select output result from computation modules; 1 Flipflop module to retain previous result; 1 reset module to reset the value in flipflop to all zero; 1 buffer module between Flipflop module and computation modules to improve the performance of driving fanout circuits.

## Slide 5: Add/sub
4-bit carry-ripple adder

## Slide 6: Mult/div
funnel shifter

## Slide 7: Optimization
Optimize and reduce redundant modules/circuits. E.g1. In initial design, a decoder is used. But after finish the design of add_sub module and mult_div module, there is no need to contain a decoder in the circuit since the INST[0] bit can select add/sub or mult/div in each module. And INST[1] can select add_sub or mult_div in the MUX to provide output.

## Slide 8: Optimization
Use transmission gate instead of static CMOS gate to reduce the number of transistors. E.g. use transmission gate to build a 2x1 MUX(without buffers) requiring 6 transistors instead of 16 transistors with static CMOS gate.
transmission gates are used in MUX_ADD_Mult module

## Slide 9: Optimization
M3 interconnection layer are used in subcircuit, M4 layer are used in top level; Upper metal layer reduces resistance when the wire has long distance.

## Slide 10: Optimization
Buffer module between Flipflop module and computation modules is added to reduce delay, and it improves the circuit speed (clock cycle) in HSPICE simulation.